## Slide 1
Validation of Pronghorn’s Subchannel code with EBR-II
shutdown heat removal tests.
March 21, 2023
Mauricio E. Tano & Vasileios Kyriakopoulos
Computational Scientists

## Slide 2: Outline
Motivation
Benchmark Description
Subchannel Results

## Slide 3: Motivation

## Slide 4: Overview
  The system level thermal hydraulic analysis codes like RELAP, RETRAN, ATHLET are used to get the balance of plant behavior.
  The results of this analysis give the boundary conditions used for the core level/component analysis.
  The detailed analysis of the reactor core is performed using the sub-channel thermal hydraulic codes.
A sub-channel is defined as the ideal flow passage formed between number a of rods or some rods and wall of channel/shroud tube
Subchannel codes are thermal-hydraulic codes that offer an efficient compromise for the simulation of a nuclear reactor core, between CFD and system codes

## Slide 5: Context
Pronghorn is an engineering-scale, coarse-mesh, thermal-hydraulics tool for supporting reactor-core simulations of advanced nuclear reactors
Most of the current efforts in Pronghorn have been devoted to developing porous finite-volume capabilities and adapted closure correlations for coarse-mesh thermal-hydraulics modeling
However, for liquid-metal reactors (LMRs) involving wire-wrapped fuel assemblies, pin-level thermal hydraulic resolution is required for most safety cases (pin rupture, channel blockage, etc.)
For this purpose, a new subchannel solver is developed in MOOSE, which allows us to solve the inter-pin flow field while still preserving an engineering-scale approach
This new solver can be natively coupled to Pronghorn and other MOOSE objects to enable full-core, multiphysics, multi-fidelity engineering studies

## Slide 6: Principles of subchannel formulation
Wire-wrapped fuel assembly
CFD simulation
Subchannel model
Resolves:
Mass, momentum (axial and cross directions), and energy balance
Requires:
Closure correlations for friction factors, localized pressure losses, and heat exchange coefficients

## Slide 7: Expansion of Pronghorn’s Subchannel code to Sodium Fast Reactors
Wire-wrapped fuel assembly
Subchannel model
Subchannel Code Resolves:
Mass, momentum (axial and cross directions), and energy balance
Requires:
Closure correlations for friction factors, localized pressure losses, and heat exchange coefficients
CFD model
ORNL 19-pin benchmark
Toshiba 37-pin benchmark
THORS blockage benchmark
Validation

## Slide 8: EBR-II
Reactor/Subassembly Geometry and Boundary conditions
EBR-II Plant Schematic

## Slide 9: Test Description

## Slide 10: SHRT-17, SHRT-45R Tests
The Shutdown Heat Removal Test (SHRT) program was carried out in EBR-II between 1984 and 1986.
On June 20, 1984, the SHRT-17 loss of flow test, was conducted where a loss of electrical power to all the plant sodium coolant pumps was used to demonstrate the effectiveness of natural circulation cooling characteristics.
Starting from full power and flow, both the primary and intermediate-loop coolant pumps were simultaneously tripped and the reactor was scrammed to simulate a protected loss-of-flow accident.
Temperatures in the reactor quickly rose to high, but acceptable levels as the natural circulation characteristics cooled the reactor down safely at decay heat levels.
Similarly to SHRT-17, the SHRT-45R test was initiated by a trip of the primary and intermediate pumps under the rated-power condition at 60.0 MW, but without scram.
EBR-II Primary Tank Sodium Flow Paths

## Slide 11: Instrumented Subassemblies (XX09 & XX10)
There are two instrumented subassemblies in the reactor core, which are labeled as XX09 and XX10.
The XX09 is a kind of driver subassembly loaded in the 5th row (4th ring) and the XX10 is a specific subassembly of which fuel pins are replaced by stainless steel pins.
the XX09 subassembly contains 61 pins wound by wire spacers. Diameters of the cladding and wire are 4.419 mm and 1.244 mm, respectively. Two out of the 61 pins contain flow meters instead of fuel slugs.
SHRT-17 Core Loading Pattern (First 8 Rows)

## Slide 12: Instrumented Subassemblies Layout (XX09 & XX10)
SHRT-17 Core Loading Pattern (First 8 Rows)
SHRT-45R Core Loading Pattern (First 8 Rows)

## Slide 13: Instrumented Subassembly XX09

## Slide 14: Instrumented Subassembly XX09
XX09 Instrumented subassembly instrument loading

## Slide 15: Boundary Conditions

## Slide 16: Subchannel Results

## Slide 17: Models of XX09
Pronghorn
Subchannel
Domain-Overlapping

## Slide 18: Pronghorn solution, steady state SHRT-17
Fluid temperature field
Linear heat flux on Pronghorn/Subchannel interface

## Slide 19: Results of Subchannel Initial Steady State for XX09 SHRT-17

## Slide 20: Results of Subchannel Initial Steady State for XX09 SHRT-17

## Slide 21: Results of Subchannel Initial Steady State for XX09 SHRT-45R

## Slide 22: Results of Subchannel Transient for XX09
Mochizuki, H., & Muranaka, K. (2018). Benchmark analyses for EBR-II shutdown heat removal tests SHRT-17 and SHRT-45R–(1,2) subchannel analysis of instrumented fuel subassembly. Nuclear Engineering and Design, 330, 14-27.